## Slide 1: SMART SCALE Process and Round 6 Update
Brooke Jackson, P.E.

## Slide 2
Agenda/Contents
SMART SCALE FY 2026 Round 6 Overview
Process Overview and Support
Performance-Based Planning
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
  Initial High-level Considerations or Project Characteristics that identify a benefit/high-scoring project
  Detailed Computations of Project Benefit and SS Score
Appendix
  C.1 Throughput (BPR) Highway calculations
  C.2 Delay (BPR) Highway calculations
  Accessibility Lookup Table
Today’s Goal: 1. Confidence in the transparent process 2. Understand and utilize resources 3. Quality projects are identified through performance-based planning, and scoring details are secondary

## Slide 3: SMART SCALE FY 2026 (Round 6) Summary and Comparison to Prior Rounds
*Total of scored applications funding requested
SMART SCALE FY 2026 (Round 6) Overview

## Slide 4: Funding Available in millions for FY 2026 (Round 6)
District | DGP Available | Previous DGP Cost Increases | HPP Available
Bristol | $37.0 |  | 
Culpeper | $68.0 | -$6.6 | 
Fredericksburg | $76.2 |  | 
Hampton Roads | $121.6 |  | 
Lynchburg | $85.9 |  | 
Northern Virginia* | $97.4 |  | 
Richmond | $104.9 |  | 
Salem | $64.3 |  | 
Staunton | $39.4 | -$6.0 | 
Statewide HPP |  |  | $384.7
Total | $694.6 |  | $384.7
A total of $1.08 billion is available for Round 6
Background information for the FY2026 – 2031 planning period
  VDOT CFO Presentation (pdf)
  VDOT CFO Presentation (YouTube)
Budget is still in flux depending on remaining needs through May
*Note: Supplemental DGP from additional gas tax in localities is not captured in NOVA District
SMART SCALE FY 2026 (Round 6) Overview

## Slide 5: Staff Recommended Funding Scenario Summary - $ in millions
SMART SCALE FY 2026 (Round 6) Overview
District | Number of Applications | DGP Available | Previous DGP Cost Increases | HPP Available | DGP Allocated | DGP Remaining | HPP Allocated | HPP Remaining | Funded in Staff Scenario | Total Allocated
Bristol | 20 | $37.0 |  |  | $27.2 | $9.8 | $0.0 |  | 3 | $27.2
Culpeper | 24 | $68.0 | -$6.6 |  | $57.0 | $4.3 | $36.4 |  | 4 | $93.5
Fredericksburg | 34 | $76.2 |  |  | $73.5 | $2.7 | $16.8 |  | 4 | $90.3
Hampton Roads | 31 | $121.6 |  |  | $111.9 | $9.7 | $27.3 |  | 11 | $139.2
Lynchburg | 12 | $85.9 |  |  | $82.4 | $3.5 | $0.0 |  | 4 | $82.4
Northern Virginia | 23 | $97.4 |  |  | $88.7 | $8.8 | $0.0 |  | 4 | $88.7
Richmond | 65 | $104.9 |  |  | $82.6 | $22.2 | $255.8 |  | 14 | $338.5
Salem | 34 | $64.3 |  |  | $53.9 | $10.3 | $0.0 |  | 3 | $53.9
Staunton | 27 | $39.4 | -$6.0 |  | $25.3 | $8.1 | $44.7 |  | 6 | $69.9
Statewide HPP |  |  |  | $384.7 |  |  |  |  |  | 
Total | 270 | $694.6 |  | $384.7 | $602.5 | $79.5 | $381.0 | $3.6 | 53 | $983.6
Starting Total | $1,079.3 |  |  |  |  |  |  |  |  | 
Remaining Total | $83.1 |  |  |  |  |  |  |  |  | 

## Slide 6: Staff Recommended Scenario – Fredericksburg
SMART SCALE FY 2026 (Round 6) Overview
Display ID | Organization | Name | Area Type | Benefit | Total Cost | SMART SCALE Request | SS Score | Fund Eligibile | (1) DGP | (2) HPP
11663 | Caroline County | Paige and Marye Route 1 Intersection | D | 19.63 | $ 7,085,483 | $ 7,085,483 | 27.71 | DGP | $ 7,085,483 | 
11661 | Caroline County | Turn Lanes at Lake Caroline | D | 9.25 | $ 9,043,110 | $ 9,043,110 | 10.23 | DGP | $ 9,043,110 | 
11640 | GWRC | Rt 3 Pipeline Old Plank Road to Salem Church Rd | B | 10.81 | $ 16,803,447 | $ 16,803,447 | 6.43 | HPP |  | $ 16,803,447
11624 | Spotsylvania County | US Rte.1 Southpoint Pkwy Intersection Improvements | B | 32.41 | $ 68,659,081 | $ 57,371,621 | 5.65 | BOTH | $ 57,371,621 | 
11664 | Caroline County | Rte 207 Sidewalk improvements at Rte 1 and Welcome Way | D | 6.95 | $ 12,689,428 | $ 12,689,428 | 5.48 | DGP |  | 
11806 | Mathews County | Rte. 3 and Rte. 198 Intersection and Road Segment | D | 1.15 | $ 2,902,789 | $ 2,902,789 | 3.95 | DGP |  | 
11769 | Gloucester County | Rte. 17 and Belroi Road Intersection | D | 2.12 | $ 6,370,284 | $ 6,370,284 | 3.33 | DGP |  | 
11627 | Spotsylvania County | Route 639 STARS Study Improvements | B | 4.58 | $ 15,682,894 | $ 15,682,894 | 2.92 | DGP |  | 
11552 | Stafford County | Route 1 and Foreston Woods Dr / Coal Landing Rd Improvements | B | 4.81 | $ 21,901,719 | $ 18,901,719 | 2.55 | DGP |  | 
11662 | Caroline County | Route 1 Ladysmith Road | D | 4.14 | $ 17,564,099 | $ 17,564,099 | 2.36 | DGP |  | 
11641 | GWRC | Warrenton Road Widening | B | 7.01 | $ 32,526,091 | $ 32,526,091 | 2.16 | HPP |  | 
11756 | Middlesex County | Rt 17-Rt 616 Town Bridge Road Int. and Segment Improvements | D | 1.55 | $ 7,524,673 | $ 7,524,673 | 2.07 | DGP |  | 
11625 | Spotsylvania County | Route 3 (Plank Road) Widening Improvements | B | 5.40 | $ 40,685,514 | $ 26,685,514 | 2.02 | BOTH |  | 
11817 | King William County | Venter Road-Rt. 30 Intersection | D | 0.84 | $ 4,844,570 | $ 4,844,570 | 1.74 | DGP |  | 
11780 | Gloucester County | Rte 17 Widening - Tidemill to Guinea | D | 11.13 | $ 64,804,111 | $ 64,804,111 | 1.72 | BOTH |  | 
11620 | FAMPO | Rt 208 Pipeline Study Corridor Improvements: Leavells Rd | B | 5.43 | $ 35,750,817 | $ 31,650,817 | 1.71 | HPP |  | 
11556 | Stafford County | Garrisonville Road Widening Phase 1 | B | 11.54 | $ 100,013,733 | $ 67,780,327 | 1.70 | BOTH |  | 
11692 | Essex County | Brays Fork Continuous Green-T | D | 3.54 | $ 23,688,008 | $ 23,688,008 | 1.49 | DGP |  | 
11626 | FAMPO | Rte 208 Pipeline Study Corridor Improvements - Smith Station | B | 4.88 | $ 45,180,736 | $ 41,180,736 | 1.19 | HPP |  | 
11554 | Stafford County | Route 1 and I-95 / Coachman Circle Safety Improvements | B | 3.93 | $ 40,869,875 | $ 37,378,274 | 1.05 | DGP |  | 
11637 | GWRC | Enon Road/Centreport Parkway Connector | B | 5.36 | $ 57,472,613 | $ 51,472,613 | 1.04 | HPP |  | 
11730 | Fredericksburg City | Lafayette Blvd Sidewalks | B | 1.25 | $ 13,541,373 | $ 13,541,373 | 0.92 | DGP |  | 
11553 | Stafford County | Route 1 and Potomac Hills LTL and Route 1 Corridor Safety | B | 1.45 | $ 16,201,266 | $ 16,201,266 | 0.90 | DGP |  | 
11804 | Westmoreland County | Route 205 at Longfield Road Intersection – North | D | 0.68 | $ 7,721,431 | $ 7,721,431 | 0.89 | DGP |  | 
11633 | FAMPO | Butler Rd Widening from Castle Rock Dr to Carter St | B | 9.22 | $ 104,752,018 | $ 104,752,018 | 0.88 | HPP |  | 
11623 | Spotsylvania County | Harrison Road / Lafayette Blvd Intersection Improvements | B | 1.23 | $ 22,063,205 | $ 14,762,492 | 0.83 | DGP |  | 
11634 | FAMPO | I-95 four-Lane Widening SB B/T Exit 130 and Exit 126 | B | 10.31 | $ 147,449,966 | $ 146,368,600 | 0.70 | HPP |  | 
11821 | King William County | Rt. 30 Bicycle/Pedestrian Improvements | D | 1.75 | $ 25,222,042 | $ 25,222,042 | 0.69 | DGP |  | 
11639 | GWRC | I-95/ Exit 136 Interchange/Centreport Parkway to Rt 1 | B | 4.45 | $ 71,639,895 | $ 71,639,895 | 0.62 | HPP |  | 
11753 | Middlesex County | Town Bridge Rd Roadway Improvements (RRR) | D | 0.65 | $ 12,802,569 | $ 12,802,569 | 0.51 | DGP |  | 
11767 | Gloucester County | Providence Rd-Rte 17 (Turn Lane) and Multimodal Improvements | D | 0.24 | $ 5,481,489 | $ 5,481,489 | 0.43 | DGP |  | 
11820 | Lancaster County | Rt 3 and Rt 794 Intersection Improvement | D | 0.09 | $ 2,230,220 | $ 2,230,220 | 0.39 | DGP |  | 
11711 | Fredericksburg City | Route 3 Intersection Improvements and VCR Trail Bridge | B | 0.50 | $ 16,229,302 | $ 15,656,249 | 0.32 | DGP |  | 
11693 | Essex County | White Oak Dr. to Teakwood Dr. Sidewalk and Crosswalks | D | 0.46 | $ 14,314,278 | $ 14,314,278 | 0.32 | DGP |  | 

## Slide 7
SMART SCALE FY 2026 (Round 6) Overview
District | # | Ave Req | Ave Cost | Cong | Saf | Acc | Env | EcD | LUM | Ave Benefit
Bristol | 20 | $ 14.5 | $ 14.5 | 0.01 | 1.33 | 0.04 | 0.18 | 0.70 | 1.16 | 2.70
Culpeper | 24 | $ 33.0 | $ 33.0 | 0.20 | 4.40 | 1.17 | 1.17 | 0.51 | 1.35 | 10.55
Fredericksburg | 34 | $ 29.5 | $ 32.1 | 0.82 | 2.33 | 0.87 | 0.18 | 0.87 | 1.10 | 5.55
Hampton Roads | 31 | $ 20.9 | $ 23.3 | 1.24 | 2.09 | 1.48 | 0.37 | 0.34 | 1.21 | 6.55
Lynchburg | 12 | $ 24.6 | $ 24.6 | 0.21 | 2.11 | 0.11 | 0.23 | 1.19 | 1.09 | 4.08
Northern Virginia | 23 | $ 57.8 | $ 81.1 | 1.86 | 1.30 | 2.62 | 1.24 | 0.05 | 1.36 | 9.68
Richmond | 65 | $ 33.7 | $ 39.6 | 1.17 | 3.10 | 2.34 | 0.86 | 1.67 | 1.27 | 11.66
Salem | 34 | $ 36.5 | $ 37.2 | 0.08 | 2.17 | 0.36 | 0.25 | 0.33 | 1.20 | 3.69
Staunton | 27 | $ 14.0 | $ 15.3 | 0.21 | 1.33 | 0.31 | 0.46 | 1.09 | 1.33 | 4.60
Grand Total | 270 | $ 30.3 | $ 34.5 | 0.75 | 2.38 | 1.25 | 0.58 | 0.85 | 1.24 | 7.33
District | # | Ave Req | Ave Cost | Cong | Saf | Acc | Env | EcD | LUM | Ave Benefit
Bristol | 3 | $ 9.1 | $ 9.1 | 0.02 | 3.68 | 0.04 | 0.25 | 1.79 | 1.19 | 6.48
Culpeper | 4 | $ 23.4 | $ 23.4 | 0.23 | 5.39 | 0.64 | 2.68 | 1.13 | 1.53 | 15.74
Fredericksburg | 4 | $ 22.6 | $ 25.4 | 3.56 | 7.63 | 2.61 | 0.72 | 2.45 | 1.06 | 18.02
Hampton Roads | 11 | $ 12.7 | $ 12.8 | 2.81 | 3.13 | 2.92 | 0.58 | 0.25 | 1.25 | 11.53
Lynchburg | 4 | $ 20.6 | $ 20.6 | 0.17 | 4.93 | 0.30 | 0.34 | 0.04 | 1.06 | 6.20
Northern Virginia | 4 | $ 22.2 | $ 23.3 | 2.59 | 0.84 | 3.05 | 3.15 | 0.07 | 1.55 | 14.79
Richmond | 14 | $ 24.2 | $ 28.7 | 1.44 | 4.63 | 4.59 | 1.15 | 3.74 | 1.31 | 19.76
Salem | 3 | $ 18.0 | $ 18.0 | 0.00 | 4.55 | 0.00 | 0.00 | 0.00 | 1.10 | 4.95
Staunton | 6 | $ 11.7 | $ 12.7 | 0.70 | 1.29 | 1.00 | 1.30 | 2.88 | 1.43 | 10.31
Grand Total | 53 | $ 18.6 | $ 20.2 | 1.54 | 3.90 | 2.43 | 1.11 | 1.75 | 1.29 | 13.56
Round 6 Applications
Round 6 Funded Applications
Statewide Comparison Benefit and Cost

## Slide 8: Virginia Code§ 33.2-214.1
Process Overview and Support
Benefit-Cost Relationship
Six Factor Areas Required (SCALE) – safety, congestion mitigation, accessibility, land use*, economic development, and environmental quality
Multi-Modal Project Evaluation – must consider highway, transit, rail, roadway, technology operational improvements, and transportation demand management strategies
Meet a VTrans Need
Projects must be fully funded when added to the SYIP
*Note: Land Use is required in populations over 200,000 defined in the 6th enactment clause

## Slide 9
Benefit Consider Area Type Weighting
Process Overview and Support

## Slide 10: Project Selection Process
Process Overview and Support
Step 1 – Fund top-scoring projects within each district eligible for Highway Construction District Grant Program (DGP) funds using DGP funds until the remaining funds are insufficient to fund the next highest-scoring project.
  DGP eligibility pertains only to localities addressing a VTrans need
Step 2 – Fund remaining top-scoring projects statewide that are eligible for Highway High-Priority Projects Program (HPP) funds using HPP funds until the remaining funds are insufficient to fund the next highest-scoring project.
  HPP eligibility pertains to localities, transit agencies, and regional entities addressing a VTrans need on either a Corridor of Statewide Significance (CoSS) or a Regional Network (RN), and refined policy definitions

## Slide 11: Scorecard Example
Process Overview and Support

## Slide 12: Support Available
Process Overview and Support
VDOT District Staff
Previous Staff, Scorers, Consultants
SMART SCALE Website
  Resources
  Previous Round Data
  Technical Guide
SMARTPortal – Public Visibility
  Scorecards
Town Halls, CTB Meetings
Trainings at Round Open
Quarterly MPO Meetings
https://smartscale.virginia.gov/resources/

## Slide 13
Interact VTrans - vtrans.virginia.gov/
P4P - vdotp4p.com
  VDOT TMPD-Managed Data repository site
  Virginia Roads for Crash Data - virginiaroads.org
U.S. Census On the Map
Population Density, Points of Interest (HERE)
  ArcGIS Online Map Population Density
  Open Street Map Data
Economic Development – VEDP Sites
VDOT Tools Homepage - vdot.virginia.gov/doing-business/tools/
  VDOT Junction Screening Tool – VJuST
  VDOT Online Forms
Virginia Open Data Portal - https://data.virginia.gov/
Applicant-Provided Data - Regional Travel Demand Models, Traffic and Planning Studies – Volumes and Growth
Publicly Available Data Sources
Process Overview and Support

## Slide 14
Regional Organizations Adopting SMART SCALE Like Processes
Central Virginia Transportation Authority (CVTA) - Regional Project Selection and Allocation Framework Page 9/PDF Page 11
Staunton-Augusta-Waynesboro Metropolitan Planning Organization (SAWMPO) - Chapter 6: Performance-Based Programming and Project Evaluation
  In Round 6, Staunton and Richmond District captured 11 of 14 HPP Projects.
Process Overview and Support

## Slide 15
  VTrans Prioritized Needs - Benefit score is project's impact to needs/problems
  Identify the Right Solutions to Needs – Value Engineering
  Cost Effectiveness
Performance-Based Planning
Performance-Based Planning

## Slide 16: VTrans Prioritized Needs
ANY Mid-Term Need is acceptable for SMART SCALE
Locations with the greatest needs are VTrans Prioritized Needs
  Priority 1 and 2 locations established in VTrans become eligible for study funding under the Project Pipeline program
Priority Needs are ranked 1 - worst 1%, 2 – worst 5%, 3 – worst 15%, 4 - remaining
Performance-Based Planning

## Slide 17: VTrans Prioritized Needs Construction District Priority
https://vtrans.virginia.gov/interactvtrans/map-explorer
Priority 1 is highest need (red)
43 out of 53 (80%) of all Funded Statewide were located on a Priority 1 or 2 Construction District Priority Need
14 out of 14 (100%) of HPP Projects Funded Statewide were located on a Priority 1 or 2 Construction District Priority Need
Performance-Based Planning

## Slide 18: VTrans Prioritized Needs Construction District Priority
Funding Comparison by District
Performance-Based Planning
35% Success Rate
19% Success Rate
10% Success Rate
 |  | Priority 1 |  |  | Priority 2 |  |  | All Other Locations |  | 
District | Total Apps | Total | Funded | Not Funded | Total | Funded | Not Funded | Total | Funded | Not Funded
Bristol | 9 | 3 | 1 | 2 | 4 | 0 | 4 | 2 | 0 | 11
Culpeper | 18 | 6 | 2 | 4 | 12 | 2 | 10 | 0 | 2 | 6
Fredericksburg | 21 | 6 | 2 | 4 | 14 | 1 | 13 | 1 | 1 | 13
Hampton Roads | 21 | 11 | 6 | 5 | 8 | 3 | 5 | 2 | 3 | 10
Lynchburg | 6 | 1 | 1 | 0 | 4 | 2 | 2 | 1 | 2 | 6
Northern Virginia | 14 | 8 | 3 | 5 | 6 | 1 | 5 | 0 | 1 | 9
Richmond | 42 | 18 | 6 | 12 | 22 | 6 | 16 | 2 | 6 | 23
Salem | 22 | 5 | 0 | 5 | 15 | 1 | 14 | 2 | 1 | 12
Staunton | 20 | 12 | 4 | 8 | 8 | 2 | 6 | 0 | 2 | 7
 |  | 70 | 25 | 45 | 93 | 18 | 75 | 10 | 18 | 97

## Slide 19
Right size the application scope (corridor size) to the worst performance locations
Planning Studies to determine Preferred Alternative
  Incorporate STARS (https://www.vdot.virginia.gov/projects/project-planning/stars-projects/) and Pipeline (https://vaprojectpipeline.virginia.gov) program methodologies
  Consider most cost-effective solution in preferred alternative selection
Frequently, the solution has already been determined, value engineering not considered
  Identify the Right Solutions to Needs – Value Engineering
Performance-Based Planning

## Slide 20
Cost Effectiveness
Cost Estimates
  Work with VDOT District early and often
  Reduce risk and contingency
If possible, apply when ready for last dollars
Performance-Based Planning

## Slide 21
Cost Effectiveness
Chart: 
| Average Request | Average Request w/ Leverage
Scored Projects | 30257796.0815 | 39048341.3247
Funded Staff Scenario | 18558154.4906 | 20529972.5625
Applicants are not “buying down” the requested amount with leverage
Performance-Based Planning
  Average Funded Project Request Round 6 – $18.6M (all) and $27.2M HPP

## Slide 22: Key Takeaways
  Focus on Priority 1 & 2 locations
  Value Engineer Solutions
  Partnership in cost estimate preparation
  Not what percent you leverage; it is what amount is requested
Acknowledge reasons why performance-based planning is overlooked
  Local board members expect an application in their district
  Pressure to apply for maximum application limit cap
  Complaints received in an area that is perceived issue, but doesn’t have supporting historical data
  Solution has already been determined; value engineering not considered
Performance-Based Planning

## Slide 23: Project Example
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1) used to illustrate how the SS Application is reviewed and scored
  Initial High-level Considerations or Project Characteristics that identify a benefit/high scoring project – key information for applicant to consider
  Detailed Computations of Project Benefit and SS Score

## Slide 24: General Information
Scope: Widen approx. 0.8 miles WB/1.05 miles EB of Garrisonville Rd between Parkway Blvd and Eustace Rd (from 2 lanes to 3 lanes) and convert Garrisonville Rd/Parkway Blvd to a signalized Continuous-Green T. Includes medians, turn lanes, new sidewalks, new crosswalks, and bus stop improvements.
Cost: $100M total, $68M requested, $32M leveraged
Eligibility: Both DGP and HPP funding
Project is in Area Type B
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Factor | Safety | Congestion | Accessibility | Land Use | Econ Dev | Environmental
Value for Area Type B | 20% | 25% | 25% | N/A* | 20% | 10%
Reminder: Land Use score is based on a multiplier and does not have a set value. The multiplier is normalized statewide between 0 and 1.
Stafford County

## Slide 25
Performance – VTrans Priority
Garrisonville Road Project - Entire study area is Construction District Priority 4
Based on this priority rating, it is a below-average need location
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)

## Slide 26
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
EPDO of Fatal and Injury Crashes S.1
Initial High-level Considerations
Refer to Virginia Roads, filter to 2019-2023 and remove PDO
Many (24) B injury crashes, a few (3) A injury crashes, a few pedestrian ~4
Consider most impactful Crash Modification Factors in high-level – CGT, Widening at Int, Median, Sidewalk
  CMF range (0.6 – 0.85), so let’s assume 0.7 generally
[(24 B * 20 EPDO * 0.7 CMF = 336) + (3A * 170 EPDO * 0.7 CMF = 357)] / Divide by 5 Years = 140 EPDO Crashes/Year. This means less than 1 K or A crash or about 7 B crashes per year will be avoided.
Area Type B
Possible Benefit Points = 14

## Slide 27
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
EPDO of Fatal and Injury Crashes S.1
Detailed Computations
Segment roadway by uniform improvement type to use for Crash Modification Factors CMF identification
Area Type B
Possible Benefit Points = 14

## Slide 28
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
EPDO of Fatal and Injury Crashes S.1
Detailed Computations
Identify Crash Modification Factors
Area Type B
Possible Benefit Points = 14

## Slide 29
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
EPDO of Fatal and Injury Crashes S.1
Detailed Computations
Apply Crash Modification Factors (maximum of three per segment)
Area Type B
Possible Benefit Points = 14

## Slide 30
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
EPDO Rate of Fatal and Injury Crashes S.2
High-level Concept
Combine in AADT, consider the lower the AADT the higher the rate per crash
5-year crashes - (24 B * 20 EPDO * 0.7 CMF = 336) + (3A * 170 EPDO * 0.7 CMF = 357) = 693
AADT to VMT = 57, 432 * 0.8 miles * 365 days * 5 years = 83,850,720
Crash Rate = (Number of Crashes) / (Total Vehicle Miles Traveled) * 100,000,000
Crash Rate per 100,000,000 miles = (693 / 83,850,720) * 100,000,000 = 826
Area Type B
Possible Benefit Points = 6

## Slide 31
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
EPDO Rate of Fatal and Injury Crashes S.2
Detailed Computations
Area Type B
Possible Benefit Points = 6

## Slide 32
  Use the attribute information to gather the 2030 V/C, slightly over capacity, would expect the bottom 10% for throughput
  Are we moving a bottleneck? Existing there are three lanes East of Eustace and two lanes west of Parkway Boulevard
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Throughput C.1 – Highway
Initial High-level Considerations
Area Type B
Possible Benefit Points = 12.5

## Slide 33
No Congestion Impact Projects
Turn lane extensions ⮽
Traffic signal retiming or traffic signal coordination projects ⮽
Installation of dynamic flashers, rumble strips, or improved signage ⮽
Widening shoulders
  the inside (left) of a freeway or divided multi-lane highway (lateral clearance always assumed to be 6 feet) ⮽
  outside (right) shoulder of a freeway or multi-lane highway if the existing lateral clearance is 6 feet or greater ⮽
Vertical or horizontal curve realignment without widening the lane or shoulder widths ⮽
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Scoring General
Initial High-level Considerations – No Impact Projects
Area Type B
Possible Benefit Points = 12.5

## Slide 34
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Person Throughput C.1 – Highway
Detailed Computations
Change in corridor total (multimodal) person throughput attributed to the project, seven years in the future.
The Highway calculations are semi-automated through the use of 3 tools
Volumes and growth are provided via applicant studies, if not, we use P4P
  Segment and intersection analysis, methodologies are outlined in the technical guide Chapter 7 referencing Highway Capacity Manual 6 methodologies, which is the basis for our in-house developed tools
    For Segment analysis - Bureau of Public Roads (BPR) equations. Nationally, the BPR equation is the mostly widely used volume-delay function for road segments.
      You can hand-calculate these measures, and this BPR example is provided in the Appendix
    For Intersection analysis – use FHWA Cap-X evaluation tool that uses critical lane volumes (CLV) to evaluate the efficiency of intersections and interchanges
  Applicant-Provided Travel Demand Model – for new alignments, widenings greater than 1 mile
Area Type B
Possible Benefit Points = 12.5

## Slide 35
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Throughput C.1 – Highway
Initial High-level Considerations
Area Type B
Possible Benefit Points = 12.5
Intersection level, applicant can reference the VDOT provided VJust Tool
Pulled from applicant-provided study
From this, selected 3-lane CGT
  Pay attention to existing V/C, less than 1

## Slide 36
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Person Throughput C.1 – Non-SOV
Detailed Computations for Ped Volumes
Pedestrian - (AADT*k-factor) on the roadway directly adjacent and multiplying the result by a pedestrian multiplier
ArcGIS Online Map Population Density
Pedestrian Multiplier Table 5,095 people per square mile = Ped Multiplier of 0.01357
Traffic Forecast P4P
New Ped Users = 57,500*0.0926 *0.0137 = 73 person
Area Type B
Possible Benefit Points = 12.5

## Slide 37
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Person Throughput C.1 – Non-SOV
Detailed Computations for Transit
Stop-level improvements without added service are simplified to ~ 2 new users
Therefore, the total Non-SOV users added (peak period) = 78 + 2 = 80 New Users
Summary Transit Scoring if project warrants segmentation scoring (new high-capacity service, increased headway)
What is the highest volume on this roadway?
What is the highest volume of transit ridership either on the roadway route or parallel?
Reduce the roadway volume by the increase in transit ridership from the project
Area Type B
Possible Benefit Points = 12.5

## Slide 38
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Person-Hours of Delay C.2 – Highway
Initial High-level Considerations
LOS E, but travel time index is good
Look at the provided study for Operational Analysis
Area Type B
Possible Benefit Points = 12.5

## Slide 39
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Person-Hours of Delay C.2 – Highway
Initial High-level Considerations
Synchro (microsimulation) is not related to BPR/CAP-X, but if you are not seeing big improvements in Synchro analysis, there won’t be in CAP-X
Provided Study has interim year at 2031
Look at Synchro Results PM Peak
  Parkway – 10s delay improvement – New CGT
  Raintree – 20s delay improvement
  Oakridge – 65s delay improvement
  Kingsland – 5s delay improvement
  Berkshire – 5s delay improvement
  Eustace – 15s delay improvement
Note this is an intersection level only
Most (if not all) of the score for this project will come from the segment (BPR) calculations
Interim
No-Build
Interim
Build
Area Type B
Possible Benefit Points = 12.5

## Slide 40
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Congestion Person-Hours of Delay C.2 – Highway*
Detailed Computations
The decrease in person hours of delay (C.2) is calculated as the difference in person hours of delay between the No-Improvement and Improvement scenarios
As mentioned earlier, the congestion calculation is semi-automated through the use of 3 tools BPR, CAP-X, and Travel Demand Model, fed by volumes in applicant-provided studies looking 7 years in the future
BPR calculations are in the appendix
* No delay score is given for Bike and Pedestrian components
Area Type B
Possible Benefit Points = 12.5

## Slide 41
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Access to Jobs (and for Disadvantaged) A.1 and A.2
Initial High-level Considerations
  Change in average job accessibility per person (A.1)/disadvantaged populations (A.2) within 45 minutes by driving (within 60 minutes for transit, bicycle, and pedestrian projects)
  Auto/Highway Mode - Requires a change improvement speed (derived from C.2 calculation), more specifically segment (BPR).The greater the change in speed, the greater the score.
  Pedestrian – highest scores for new facilities; upgrades have a small impact
    Not eligible – 1. Replacing the existing as-is 2. Crosswalks (new or existing), except combining a NEW refuge island, pedestrian signal, push button, or HAWK/PHB/RRFB
  Transit – scores for new routes, change in headway, new/relocated stops
    Not eligible – 1. Upgrading bus stop amenities 2. Increasing capacity without changing travel time or schedule
  Receives a score for each mode with a direct improvement, example project:
    Auto/Highway ☑ Change in speed >20 mph (refer to appendix congestion ex for speed change calc)
    Pedestrian ☑New Sidewalk
    Bicycle ⮽
    Transit ⮽ - No score for amenity improvements
Area Type B
Possible Benefit Points = 15

## Slide 42
Access to Jobs A.1/A.2
Detailed Computations
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)

## Slide 43
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Access to Jobs A.1/A.2
Detailed Computations
Determine project limits and the type of improvement
  Auto, Park and Ride - change in travel speed
  Bike/Walk
    Identify adjacent roadway facility - functional class, number of lanes, and speed limit
    Check the Level of Service (LOS) value via the lookup table*, which considers the changes in speed from the congestion score and other characteristics mentioned in step 2
    Code the LOS value for base/project conditions on selected project links in the scoring tool
Define Influence/Buffer Area 45 miles around project (Auto/Transit), 10 miles Bike, 3 miles for walk
Run the tool (TransCAD) to obtain Accessibility scores by each mode type (there has to be a direct improvement to the mode to begin calculation) –
  *Please refer to Slide 74 for lookup tables.
Area Type B
Possible Benefit Points = 15

## Slide 44
The overall accessibility score for a defined catchment area is calculated using a population-weighted average of the cumulative decayed job access scores for each block group. Each block group contributes to the final score proportionally to its population.
  𝐶_𝑗𝑜𝑏_𝑛 be the cumulative decayed* job score for block group n, using the decay-weighted sum of reachable jobs,
  Pop n is the population of block group n,
  N is the total number of block groups within the catchment area.
Weight by disadvantaged populations for A.2
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Access to Jobs A.1/A.2
Detailed Computations Example
Area Type B
Possible Benefit Points = 15
Example has 44,000 census blocks
Note: Accessibility tool calculates these numbers based on a travel time decay function, where jobs within a shorter travel time are weighted more than jobs farther away. For more information on decay functions SSTI Reference-
A Guide For Transportation And Land Use Practitioners

## Slide 45
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Access to Multimodal Choices A.3
Initial High-level Considerations / Detailed Calcuation
5 Points *Non-SOV 80 = 400
Area Type B
Possible Benefit Points = 5

## Slide 46
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Project Support for Economic Development ED.1
Initial High-level Considerations
Define Search Area Distance Table 10.2
Use Google Maps to Define Search Area
Area Type B
Possible Benefit Points = 12

## Slide 47
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Project Support for Economic Development ED.1
Initial High-level Considerations
VEDP Site Search - https://sites.vedp.org
There are two properties, but no VEDP sites
  Sites are the polygons
  Score will be zero
Generalizations
  Typically, the larger the site, the higher the score
  ED.1 Round 6 results to estimate
VEDP Sites are incorporated with Portal App
  Work with VEDP ahead of Aug 1 submission if you believe there are missing sites
Site
Site
Area Type B
Possible Benefit Points = 12

## Slide 48
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Project Support for Economic Development ED.1
Detailed Computations Ex. Warrenton Road Widening (11641)
Add New Through Lanes – 3 mile search
Calculate Economic Impact Points using Historical Model
  Jobs Creation – 380 – normalize this to 40 pts
  CapEx – 490 – normalize this this to 25 pts
Funding Points (Y/N) – 15 pts Go VA, Tobacco Com, VBRSP ⮽
Project Site Visit Points – normalized to 10pts by # of visits ⮽
Highest VBRSP Tier Site –10pt ☑ Virginia Gateway Land at International Parkway is Tier 2 – 4pts
Calculate Final Measure
Area Type B
Possible Benefit Points = 12
DISPLAY_ID | Jobs | Capex | Funding Received | Site Visits | Highest VBRSP Tier Site | Normalized_Jobs | Normalized_CapEx | Funding_Points | Normalized_Visits | Tier_Points | Measure_Value | Normalized_Score
11641 | 380 | 490.93 | No | 0 | 2 | 3.45 | 1.72 | 0 | 0 | 4 | 9.17 | 10.27

## Slide 49
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Project Support for Economic Development ED.1
Historical Model Background – Linear Regression Model
  Property Size (~ 60% of score)
Geographic Location (~40% of score)
  ~15% surrounding terrain - Developed/Forest/Swamp/)
  Remaining ~20-25%
    Industry Sector (Knowledge Work/Logistics/Manufacturing)
    Wages for each industry sector w/in 45-minute drive
    Potential Employees (workforce w/ in a 45-minute drive)
    Educational pipeline – Student population and Research Universities within 20 miles
    Metropolitan Statistical Areas (MSA) Classification
    Access to Infrastructure – ports/airports within 30 miles
Utilize - https://onthemap.ces.census.gov
Area Type B
Possible Benefit Points = 12
The Historical Projects Model (HPM) is a tool to provide bulk estimates for the announced jobs and capital expenditure (CapEx) a property could generate if it were to receive an economic development project. These estimations are created by a linear regression model, which considers the size of the property and its geographic location. These figures represent the jobs and CapEx that have typically been associated with similar properties in the past.

## Slide 50
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Intermodal Access and Efficiency ED.2
Initial High-level Considerations
Key Components
Does the project improve freight access? ☑ Widening
Delay Score > 0 ☑ Yes
Freight Volume – <2% HV ~1000
Low Freight Volume is the major indicator of score
  Points range from 0-6
  Range of score is 0 – 6,000
  Round 6 high score 47,000
Area Type B
Possible Benefit Points = 4

## Slide 51
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Intermodal Access and Efficiency ED.2
Detailed Computations
Add in Point Calculation
Google Imagery Search – Distribution Facilities - Quarry ☑
ArcGIS Online STAA Routes - None = 0 ⮽
ArcGIS Online Ports and Airports – None 0 ⮽
Delay Score > 0 ☑
Freight Volume –< 2% HV ~1,200
Project length 0.8
Measure = (2+0+0) * 1,200 *0.8 = 1,920 (1,922 official score)
Area Type B
Possible Benefit Points = 4

## Slide 52
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Travel Time Reliability ED.3
Initial High-level Considerations
Point-based system, scaled by :
  P4P – Buffer Time Index Weekday = round up 0.2
  Note: SMART SCALE official score uses Buffer index (BI) from University of Maryland Regional Integrated Transportation Information System (RITIS)
  Corridor VMT – refer to S.2- AADT to VMT = 57, 432 * 0.8 miles * 365 days = 16,700,000
  BTI * VMT * [(Incident Freq, range 0-2 * EPDO Score, range 0-5) + (Weather Impact, range 0-2 * Frequency, range 0-2)]
  Range of Score 0 to 50,000,000 >> max RD 6 score was over 1 Billion, so assume small impact
Area Type B
Possible Benefit Points = 4

## Slide 53
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Travel Time Reliability ED.3
Detailed Computations
Point based system, scaled by:
  RTIS gave higher BTI at 0.24
  PDOs boosted to above 300 - 5 Points
  Max Points were given
BTI x VMT x [(Incident Freq, range 0-2 x EPDO Score, range 0-5) + (Weather Impact, range 0-2 x Frequency, range 0-2)]
= 0.24 x 16,700,000 VMT x [(2x5) + (2x2)] = 56,112,000
Official Score = 53,156,903, official difference is exact VMT
Area Type B
Possible Benefit Points = 4

## Slide 54
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Air Quality and Energy Environmental Effect E.1
Initial High-level Considerations
Part 1 (50% of Score)
Point-based system Scaled by:
New Non-SOV Users Normalized to 50 ☑ 80 New Non-SOV Users (Ped and Transit) = 3pts * 80 = 240
Peak period truck volumes IF tuck volume > 8% Normalized to 50 ⮽ ED.2 slide < 2% truck volume
Part 2 (50% of Score)
50% CO2 Offset Due to:
Increased Non-SOV VMT
        +
Due to Reduced Heavy Vehicle Hours of Delay (HVHD)
Score is going to primarily come from new ped users
Area Type B
Possible Benefit Points = 10

## Slide 55
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Air Quality and Energy Environmental Effect E.1
Detailed Computations
Part 1 (50% of Score)
Point-based system Scaled by:
New Non-SOV Users, Normalized to 50 = (3 points x 80 users = 160) normalized to 22 +
Peak period truck volumes IF tuck volume > 8%, Normalized to 50 = (0) normalized to 0
  Part 1 = 22 -> this is normalized to 17.7 x 50% of Score = 8.9
Part 2 (50% of Score)
50% CO2 Offset Due to:
Increased Non-SOV VMT = [80 users x0.67 miles average trip length] x (1 gal/24miles ) x (8.9 kgCO2/1 gal gas) = 20 kgCO2 gets normalized to
Due to Reduced Heavy Vehicle Hours of Delay (HVHD) = [2% Trucks x120.6 Delay red/(1.2 Persons/Vehicle)]x 0.44 x 8.9 = 8 kgCO2 gets
  Part 2 = 28 total kgCO2 ,Normalized to 4.5 x 50% of Score = 2.25
  Part 1 and Part 2 Combined Score = 11
Refer to Oct 2021 CTB Presentation, Dec 2021 CTB Presentation for a more examples and information
Area Type B
Possible Benefit Points = 10

## Slide 56
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Impact to Natural and Cultural Resources - E.2
High-level Concept
Identify if project is low impact:
Project length/size 0.8 miles
Type of Project (Table 9.3) buffer area – Tier 3, ¼ mile
Type of Document (Chapter 12.0 of Tech Guide) – CE = 10%
Maximum Possible Impact Area = (0.8 mile * 0.25 mile) * 640 ac/sq mile * 10% = 12.8 acres
“Top” Score was 117, so maximum subtraction 0.5pts, but will most likely be less
Impact Area is overlaid with Natural/Cultural Resources layers (Next Slide)
Area Type B
Possible Benefit Points = -5

## Slide 57
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Impact to Natural and Cultural Resources - E.2
Background Information
This data is protected by individual data-sharing agreements directly with each agency and can be engaged on an agency level. Publicly Available
Conservation Lands
  Appalachian Trail Conference Appalachian Trail
  Virginia Outdoor Foundation Protected Easements
  Virginia Department of Conservation and Recreation Conservation Land
  Virginia Department of Conservation and Recreation 6F properties
  Virginia Department of Conservation and Recreation Natural Heritage Screening Sites
  Virginia Department of Forestry Agricultural/Forest Districts
Species/Habitat
  Virginia Department of Wildlife Resources Threatened and Endangered Species
  Virginia Department of Wildlife Resources – Bats and Roost Trees
Cultural Resources
  National Park Service, American Battlefield Protection Program Potential National Register (POTNR) Areas
  Virginia Department of Historic Resources Architecture layer: properties listed in or determined eligible for listing in the National Register of Historic Places (“NRE Eligibility Status”)
  Virginia Department of Historic Resources Archeology layer: sites listed in or determined eligible for listing in the National Register of Historic Places (“NRE Eligibility Status”)
  Virginia Department of Conservation and Recreation Conservation Lands (Managing Agency= Virginia Department of Historic Resources)
Wetlands
  U.S. Fish and Wildlife Service National Wetlands Inventory
Area Type B
Possible Benefit Points = -5

## Slide 58
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Future Transportation Efficient Land Use - L.1/L.2 (Horizon)
Initial High-level Considerations
Area Type B
1 – 2 Multiplier
Geographic Scope is the number one influence for score:
ArcGIS Online Map Population Density within one-mile
Non-Work Destinations within one-mile walk (HERE official)
New walk connections made by project
Map with Census density data and Open Street point-of-interest data

## Slide 59
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
Future Transportation Efficient Land Use - L.1/L.2 (Horizon)
Detailed Computations
Area Type B
1 – 2 Multiplier
Uses Accessibility Tool in TransCAD
Runs the walk module with 1-mile buffer
Non-work destinations, scaled by type
Assign LOS Change – same method as Accessibility Team (Slide 74)

## Slide 60: Scorecard
Example Project – ID 11556 (Garrisonville Rd Widening Phase 1)
12.5%
12.5%
14%
6%
15%
5%
5%
12%
4%
4%
10%

## Slide 61: Next Steps
February to May – Board to consider potential revisions to staff-recommended funding scenario
May 6 – Fredericksburg FY2026-2031 Six-Year Improvement Program Spring Meetings
May CTB meeting – Consensus funding scenario developed
June CTB meeting – Adoption of Six-Year Improvement Program and SS Round 6 projects

## Slide 62: Contact Us
Brooke Jackson, P.E. – SMART SCALE Program Manager
  Brooke.Jackson@oipi.virginia.gov
Email - SmartPortal@CTB.Virginia.gov
Contact Form

## Slide 63: Demand Flow Rate (): Variables
  : peak hour volume—interim year peak hour volumes from provided study, scaled down to SMART SCALE Round 6 analysis year of 2030
  : direction distribution factor (d-factor)—from P4P “AADT” or “Traffic Forecast” layer
  : peak hour factor—not available on P4P, assumed value of 1.0
  : adjustment factor for presence of heavy vehicles—from Highway Capacity Manual
  : adjustment factor for atypical driver populations—default value of 1.0
  : number of travel lanes
Appendix - C.1 Throughput (BPR) Highway calculations

## Slide 64: Pathways for Planning (P4P) Layer Screenshot *Study volumes were used for the official score. AADT volumes were used in this BPR example to demonstrate the exploratory calculations that can be done using P4P data.
Appendix - C.1 Throughput (BPR) Highway calculations

## Slide 65: Demand Flow Rate (): Garrisonville Rd Inputs Peak Direction, Wolverine Wy to Dun Rovin Ln
  2 in No Improvement condition, 3 in Improvement condition
    : Proportion of heavy vehicles—not available on P4P, assumed value of 2%
    : Passenger car equivalent of one heavy vehicle—2.0 (from SMART SCALE Congestion Scoring User Manual)
Appendix a) C.1 Calculation Example

## Slide 66: Demand Flow Rate (): Calculation
No Improvement
Improvement
Appendix - C.1 Throughput (BPR) Highway calculations

## Slide 67: Person Throughput ()
  : number of persons per trip—default value of 1.20
  : roadway segment capacity, based on facility type—from SMART SCALE Congestion Scoring User Manual; value of 900 based on functional classification of Major Collector
No Improvement
Improvement
Appendix - C.1 Throughput (BPR) Highway calculations

## Slide 68: Free-Flow Speed (): Variables
  : base free-flow segment speed—from SMART SCALE Congestion Scoring User Manual; value of posted speed limit plus 7 mph
  : adjustment factor for lane width—from Highway Capacity Manual
  : adjustment factor for total lateral clearance—from Highway Capacity Manual
  : adjustment factor for median type—from Highway Capacity Manual
  : adjustment factor for access point density—from Highway Capacity Manual
Appendix - C.2 Delay (BPR) Highway calculations

## Slide 69: Free-Flow Speed (): Garrisonville Rd Inputs Peak Direction, Wolverine Wy to Dun Rovin Ln
  (11-foot lanes)
  (12-foot total lateral clearance)
  (segment has a divided median)
  (segment has an average of 3 access points per mile)
Appendix - C.2 Delay (BPR) Highway calculations

## Slide 70: Average Segment Speed ()
  : free-flow segment speed—calculated from methods in Highway Capacity Manual
  : parameter—default value of 0.2
  : parameter—default value of 10
No Improvement
Improvement
Appendix a) C.1 Calculation Example

## Slide 71: Person Hours of Delay ()
  : roadway segment length—measured from Google Maps (0.34 miles)
No Improvement
Improvement
  *if FFS > speed limit, set FFS equal to speed limit
  **if S > speed limit, D=0
Appendix - C.2 Delay (BPR) Highway calculations

## Slide 72: BPR C.1 and C.2 Measure
BPR C.2 Measure
Appendix - (BPR) Highway calculations
BPR C.1 Measure

## Slide 73
Appendix – Accessibility Lookup Table
Access to Jobs A.1/A.2
Detailed Computations
Area Type B
Possible Benefit Points = 15
  Lookup Table for Bike and Ped
  *Speed limit
*